## Slide 1: Application of Model Predictive Control for Optimal Operation of Wind Turbines
Yuan Yuan, Pei Cao, and Jiong Tang
Mar 27, 2017
SPIE Smart Structures NDE Conference 2017
Department of Mechanical Engineering
University of Connecticut
Storrs, CT, USA
Dynamics, Sensing, and Controls Laboratory
Notes: 1

## Slide 2
Wind Energy
Fastest growing renewable energy source in the world: The worldwide wind capacity reached over 400,000 MW by the end of 2015
Low cost & environmentally friendly
Wind turbine control loops
  Generator torque control
  Blade pitch control
  Nacelle yaw control
Pitch control animation
Yaw control animation
Background: Wind Turbine and Control

## Slide 3
Different control goals
Speed control
Power control
Load reduction on blades, tower and drive-train
Prolong actuator life
      Model predictive control:
      Online optimization of multiple control objectives
Multiple Objectives in Wind Turbines
Challenges of multiple objectives
  Designing individual controllers for each objective is getting more and more complex
  Conflicting with each other
  We need one controller that can balance all the objectives together
Notes: To reduce the overall cost, we have several…first we need the speed control to keep the rotor at the rated value when wind speed is very high. If the rotor is over-speed, it will cause the over-heat of the generator and make the turbine on fire as shown in the first figure.
Also we want the power control, to make sure we capture the maximum power from wind when wind speed is not that high.
In addition, we can see there are a lot of components failure, the tower may fall and blade may crack. We need to reduce the loads.
Also, the life of actuators has its limit, changing them too often will increase more costs. So that we need to prolong the actuator life.
However,…..it is quite challenging when we realize multiple objectives
In this research, we choose MPC to achieve the optimization….

## Slide 4
Control Architecture
Torque control: Standard torque control
Pitch control: Model predictive control
Yaw control: Not involved
-
Notes: The yaw control is not involved, similar to other studies.

## Slide 5
Switching Region Performance
Results:
Power: Nearly same
Speed : better
Tower fore-aft loads: reduced
Tower side-side loads: mixed
Blade edgewise loads: nearly same
Blade flapwise loads: reduced
Pitch actuator: reduced
Wind fields:
11 m/s, 12 m/s, 13 m/s

## Slide 6: Periodic Wind Disturbance Rejection using Robust Individual Control Strategy
Mar 5, 2018
Department of Mechanical Engineering
University of Connecticut
Storrs, CT, USA
Yuan Yuan, X. Chen, J. Tang
Photo by NREL

## Slide 7: Motivation1
Individual pitch control to mitigate periodic loads
Enabled by recent hardware advancements
wind
wind
upwind turbine
downwind turbine
Tower shadow
Tower top
, : prevailing wind speed at the tip of each blade
Wind shear
Tower shadow and wind shear effects
Periodic loads
different wind speed at different height

## Slide 8: Control architecture formulation
Control architecture formulation
Collective loop:
Speed and power regulation
GSPI/DOB [1]
Individual loop:
Periodic load mitigation and modeling uncertainties
Robust control with weighting function selection
[1] Yuan, Y., Chen, X., and Tang, J., 2017, "Disturbance Observer-Based Pitch Control of Wind Turbines for Enhanced Speed Regulation," Journal of Dynamic Systems, Measurement, and Control, V139(7), pp. 071006.

## Slide 9: PSD results
PSD result analysis at multiple frequencies
18 m/s turbulent wind field excitation
Significant 1P, 2P, and 4P peak reduction

## Slide 10: Load analysis
Blade and tower fatigue damage equivalent load (DEL) comparison
Collective control
PID individual control
Robust individual control
Blade flapwise: Robust: -20% of PID
Blade edgewise: same level
Tower base fore-aft: 3%-10% decrease
Tower base side-side: same level
(DEL: industrial standard)