## Slide 1
Advanced Control Design for Wind Turbines
Yuan Yuan
August 9th, 2018
Corning Incorporated
Corning, NY, USA
PhD candidate
University of Connecticut

## Slide 2: Outline
PhD work
background & Control Method
Disturbance Observed Based control
Robust control
Model predictive control
Adaptive control
Work in Corning
Model predictive control in laminated glass
Concluding Remarks

## Slide 3: Me
PhD candaite:
Mechanical Engineering, University of Conneticut, Aug, 2013- December, 2018(expected)
Master degree: Eletrical Engineering (control theory and control engineering)
Northerwestern Polytechnical Unversity, China
Bachlor degree: Electrical Engineering (automation),
Northerwestern Polytechnical Unversity, China
Hobbies: Boating, and badminton.
Current: Control scientist intern，Sullivan Park

## Slide 4
Wind Energy
Fastest growing renewable energy source in the world: The worldwide wind capacity reached over 400,000 MW by the end of 2015
Low cost & environmentally friendly
Wind turbine control loops
  Generator torque control
  Blade pitch control
  Nacelle yaw control
Pitch control animation
Yaw control animation
Background: Wind Turbine and Control
Notes: Collective individual

## Slide 5
Challenges of Wind Turbines
Source: DOE
  Goal: to reduce the cost of wind energy
  Complex dynamics
  Increased turbine size
  Complex structures: airfoil-shaped blades
  Uncertain environments
Time-varying wind speeds
Weather changes, icing, and assemblage error of turbine
Advanced controllers can help reduce maintenance cost and increase power capture

## Slide 6
Different control goals
Speed control
Power control
Load reduction on components
Prolonged actuator life
  Complex dynamics & uncertain environments
  Conflicting objectives
6
Research Objective
  Explore different control approach

## Slide 7
Operating Regions
  Maintain the rated generator speed
  Mitigate structural loads
Optimal balance between energy production performance and reliability of components
[1] Jonkman et al., National Renewable Energy Laboratory Technical Report, 2009.
  Control laws
  Disturbance observer based control
  Robust control
  Model predictive control
  Adaptive control
  Region 2: torque control[1]
  Maximum power
  Region 3: pitch control

## Slide 8
AeroDyn
An aero-elastic simulation code (by NREL) to predict the aerodynamics
Input: steady or turbulent wind file
Output: force and moment on the turbine components
Dynamic modeling
: mass matrix
: force
: control input
: wind input
: DOF displacements
: DOF velocities
: DOF accelerations
: time
Nonlinear aero-elastic equations of motion of wind turbine system

## Slide 9
    linearization
FAST (Fatigue, Aerodynamics, Structures, Turbulence)
    FAST code (by NREL) used for simulating the coupled dynamic responses of wind turbines
Model Linearization
    State space representation
    Numerically linearize the equation by perturbing (∆) each variable about their respective operating points (op):

## Slide 10
Control Architecture
Torque control: Standard torque control
Pitch control: Model predictive control
Yaw control: Not involved

## Slide 11
Baseline Gain Scheduling Proportional Integral Derivative pitch controller [1]
Baseline Pitch Control
: small perturbation of blade pitch angle about the operating point
: error between measured generator speed and rated set point value
Gain scheduling factor to accommodate time-varying operating wind condition
Gain scheduling: , are changed
[1] Jonkman et al., National Renewable Energy Laboratory Technical Report, 2009.
.
: blade pitch angle at which the pitch sensitivity is doubled from its value at the rated operating point.

## Slide 12
Outline
Background
Research Objective
Disturbance observer based control
Concluding Remarks
Future Tasks
Notes: This is an outline of my presentation, first, background

## Slide 13
Disturbance observer based control
High precision motion control
Micronano manufacturing
Advantage: great disturbance rejection performance
Promising to make improvements in wind turbine control area
Disturbance Observer Based Control
How is this control strategy tailored for complex wind turbine dynamics
Objective: speed and power control, load mitigation at some components
Notes: The utre 1……is DOB…this another good way to address speed and power control for the wind turbine..
It is actually the latest progress in high precision motion control. So far, it has been applied successfully to micronano manufacturing. But……It is highly promising to make fundamental improvement in the turbine blade control
Actualy Our preliminary result shows DOB is capable of regulating speed and power. Which is the first sucefful example of using DOB controller of wind turbine.
Let us see…
Height:10nm width 100nm
Next we will explain why this DOB controller can help

## Slide 14
:
wind disturbance
:
disturbance model
:
plant model
:
model inversion
:
filter
:
PID controller
directly cancels out
filter Q
0
den
num
Why this controller?
Gain-scheduling PID: perfect gain correction is not strictly guaranteed
Augmented controller: inner-loop can further reject low frequency disturbance based on the disturbance suppression of the outer-loop.
Disturbance Observer Based Controller
Notes: Here we quickly go through the essential details
It is an inverse-based disturbance cancelation scheme. We want to use d hat to directly cancel out d
The inner loop is the disturbance observer structure, the outter loop is the gain-scheduled PID controller. Both of them will contribute to disturbance rejection.
The P inverse should be stable
The fundamental idea is to make the differnec eto be 0
Through the equations, we can derive filter Q
For any signal d0 it will satisfy this eq. where Bd is numerator of z transofrm of d0. Ad is the corsponding den.

## Slide 15
Persistent wind disturbance input:
step disturbance
Disturbance Observer based controller
Wind disturbance: Variance between nominal wind speed and the operating wind speed
unknown amplitude, known waveform
Disturbance rejection is achieved if
Notes: We assume in this reseach, dot
Take z transform of step. And from the loop shaping of previuos control sheckem,
So under the step disturbance, we can derive the expression of d
The FIR filter K is added to ensure the causality of Q
We also introduce an extra item in the denominator, where the design of belta is used to tune the local loop shaping. based on the damped pole –zero pair pinciple.
The effect of the choice of belta will be explained in details later.
When there is no belta, the shape of Q is certain ,we can not tune it. Belta can change the shape of Q, then we can tune it. Look at the figure.

## Slide 16
5-DOF Linearized Model (Preliminary Result)
5 DOF: Generator DOF, drivetrain torsional flexiblity DOF, and first flapwise blade mode DOF (three blades)
Further analysis is needed to deal with the nonlinearities
Notes: To obtain the preliminary result of the DOB controller, we first apply the controller into the 5-DOF linearized model
These are the
The result seems to be promising, so how is it with the nonlinear plant

## Slide 17
Test wind turbine
  NREL offshore 5-MW baseline
  wind turbine
Degree of freedom (DOF)
  16 DOFs*
Turbulent wind field
Simulation time
  Run time: 0 to 600 s
  Integration step size: 0.0125 s
Blade pitch limit and pitch rate limit [1]
  Minimum/maximum blade pitch: 0 degree / 90 degree
  Maximum absolute blade pitch rate: 8 degree/s
Case Study: Nonlinear plant
Case study:
[1] Jonkman et al., 2009, National Renewable Energy Laboratory, Golden, CO.
*First flapwise blade mode (3 blades), second flapwise blade mode (3 blades), first edgewise blade mode (3 blades), drivetrain rotational-flexibility, generator, yaw, first fore-aft tower bending-mode, second fore-aft tower bending-mode, first side-to-side tower bending-mode, second side-to-side tower bending-mode.

## Slide 18
Performance comparison
Results:
3.59% - 9.56% decrease in 6 wind fields
2.38% - 8.01% increase in 3 wind fields
Limited performance due to trade-off with respect to the stability issue
Notes: This slide shows the results based on the selected Q filter
The first figure is wind speed
The second figure is the …response under 18
We can see
To test robustness of the DOB controller, we applied it to wide wind speed region from 14 to 22.
We can find there is …..
So what more we can do?

## Slide 19
under different
Trade-off in selection of Q filter
Trade-off between disturbance rejection region and disturbance amplification region:
Sensitivity function:
Disturbance amplification:
Instability of the nonlinear plant (model mismatch exists)[5]
[5] Doyle et al., Feedback Control Theory, 1990.
Notes: Here we will talk about how to make a trade off in selection of Q filter. Specifically it is the trade-off between ……
In practice, when DOB controller is applied to nonlinear controller, the disturbance amplification at high freuqencies will lead to the insatiability of …..
Actually the value of belta is related to sensitivity function. This equation in the red box is an indicator of sensitivity function. We check the fre response of it under differernt belta.
From the figure we can see the samller belta will lead to wider disturbance rejection region, but at the same time the larger disturbance amplification. Which will influence the stability of system.
Finally we choose belta =.997.

## Slide 20
Add-on compensator
Sensitivity function
Smaller disturbance amplification at certain high frequencies in Q*
Better disturbance rejection in low freq.
Faster roll-off at high frequencies
Low pass filter
Q filter (DOB)
Q* filter (DOB*)
Notes: Next we will introduce how to improve the tracking perfromance. We propose to use an add-on compes

## Slide 21
Performance comparison
FFT

## Slide 22
Performance comparison
Normalized generator speed RMS error: -28.13% to -39.14%
Normalized power RMS error: -31.43% to -40.93%
Conclusion:
Enhanced generator speed and power regulation with DOB* in Region 3

## Slide 23
Concluding Remarks
  A general disturbance observer (DOB) based controller tailored for wind turbine is developed;
  The FIR filter and a tuning factor are introduced to facilitate better design of Q filter;
  Generator speed and power regulation performance is enhanced in DOB* controller for the actual nonlinear wind turbine under turbulent wind filed;
  DOB controller shows stability robustness under the entire Region 3.
This research is supported by NSF under grant CMMI – 1300236
Notes: simulation software

## Slide 24: Periodic Wind Disturbance Rejection using Robust Individual Control Strategy
Mar 5, 2018
Department of Mechanical Engineering
University of Connecticut
Storrs, CT, USA
Yuan Yuan, X. Chen, J. Tang
Photo by NREL

## Slide 25: Motivation1
Individual pitch control to mitigate periodic loads
Enabled by recent hardware advancements
wind
wind
upwind turbine
downwind turbine
Tower shadow
Tower top
, : prevailing wind speed at the tip of each blade
Wind shear
Tower shadow and wind shear effects
Periodic loads
different wind speed at different height

## Slide 26: Motivation2
Challenges for wind turbine control:
Model uncertainties
Periodic loads on blades
Coupling dynamics of 3-bladed pitch system
Difficulties in designing controller:
Operating point varies constantly – actual dynamics is different from nominal model
Source: Liebherr
Objective:
Speed and power regulation in high wind speeds
Mitigate periodic loads
Robust stability and robust performance
Potential solution: Robust Controller (structured singular values ()-synthesis)
Notes: One potential solution is

## Slide 27: Dynamics and modeling
Bir, G.S., 2010. User's guide to MBC3: Multi-blade coordinate transformation code for 3-bladed wind turbine.
An average state-space system is obtained from the complete set of linearizations at N azimuth angles by computing
A series of LTI state space model depends on azimuth
e.g. 36 models: = 0, 10, 20,…350 deg
Periodic LTV state space model
Steady state: blade motion is a Fourier series equation
linearization
MBC transformation
Modeling including periodic dynamics
transform from rotating coordinates to nonrotating coordinates
Notes: The dynamics of wind turbine rotor blades are generally expressed in rotating frames attached to the
individual blades. The tower-nacelle subsystem sees the combined effect of all rotor blades, not the
individual blades. This is because the rotor responds as a whole to excitations such as aerodynamic gusts,
control inputs, and tower-nacelle motion—all of which occur in a nonrotating frame. Multi-blade
coordinate transformation (MBC) helps integrate the dynamics of individual blades and express them in a
fixed (nonrotating) frame. MBC involves two steps: transformation of the rotating degrees of freedom,
and transformation of the equations of motion.
MBC transformation can reduce the variations between linearizations obtained at different azimuths, and therefore yields a better representation of the turbine dynamics

## Slide 28: Uncertain model structures
Frequency responses comparison
Model mismatch in high frequency regions
Uncertain model structure formulation
Fit an uncertain model structure to an array of LTI responses :
Pick nominal model: 18 m/s
LTI state space model
Challenge: wind speed changes so actual dynamics changes
Uncertain model structures
14 m/s, 16 m/s, 20 m/s, and 22 m/s

## Slide 29: Shear components
Bode Diagram has large magnitude
Horizontal and vertical wind shear effects to dynamic modeling
Include wind shear components in the model
Magnitude of , to moments , :
70 – 80 dB
Magnitude of horizontal wind to moments , :
20 – 30 dB

## Slide 30: Control architecture formulation
Control architecture formulation
Collective loop:
Speed and power regulation
GSPI/DOB [1]
Individual loop:
Periodic load mitigation and modeling uncertainties
Robust control with weighting function selection
[1] Yuan, Y., Chen, X., and Tang, J., 2017, "Disturbance Observer-Based Pitch Control of Wind Turbines for Enhanced Speed Regulation," Journal of Dynamic Systems, Measurement, and Control, V139(7), pp. 071006.

## Slide 31: Structural singular value (-synthesis formulation
RSRP (robust stability and robust performance) guarantee under model uncertainties due to operating point variation
Disturbance rejection via weighting function selection
Advantages using structural singular value-synthesis
The performance of MIMO control systems are characterized using norms
: disturbance
: input
:output
: weighted output
G: generalized plant
K: robust controller
: perturbation of G
M- structure

## Slide 32: Power spectral density
Power spectral density (PSD) of blade 1 root flapwise moment with only collective loop
Multiple peaks at 1P (per revolution), 2P, 3P, … frequencies due to periodic loads on
1P
2P
3P
4P
Rated rotor speed:
Severe limits:
Component failure

## Slide 33: Weighting functions
Rotating coordinate | Non-rotating coordinate
1P | 0P @ and
2P | 3P@ and
3P | 3P @
4P | 3P@ and
5P | 6P@ and
6P | 6P@
7P | 6P@ and
Rotating coordinate | Non-rotating coordinate
1P | 
2P | 
3P | 
4P | 
5P | 
6P | 
7P | 
Sensitivity function
Minimize the norm
Frequency effects change due to coordinates change
Further penalize the control input and output performance

## Slide 34: Weighting functions
Select weighting functions
low frequency
low pass filter

## Slide 35: Singular values
Multivariate transfer functions: singular values of transfer function
Open-loop and closed-loop responses of the nonlinear wind turbine under turbulent wind excitations
Deal with uncertain model structure (a group of curves)
0P and 3P disturbance rejection
= 0.1784 < 1 RSRP guaranteed
Notes: The shaping of multivariate transfer functions is based on the idea that a satisfactory definition of gain for a matrix transfer function is given by the singular values of the transfer function

## Slide 36: PSD results
PSD result analysis at multiple frequencies
18 m/s turbulent wind field excitation
Significant 1P, 2P, and 4P peak reduction

## Slide 37: Load analysis
Blade and tower fatigue damage equivalent load (DEL) comparison
Collective control
PID individual control
Robust individual control
Blade flapwise: Robust: -20% of PID
Blade edgewise: same level
Tower base fore-aft: 3%-10% decrease
Tower base side-side: same level
(DEL: industrial standard)

## Slide 38: Concluding remarks
A robust controller with mu synthesis for wind turbine is developed;
Individual pitch control is utilized to reject periodic loads;
Robust control strategy is formulated to tackle with modeling uncertainties;
Periodic loads on blades are significantly reduced.

## Slide 39
Different control goals
Speed control
Power control
Load reduction on blades, tower and drive-train
Prolong actuator life
      Model predictive control:
      Online optimization of multiple control objectives
Multiple Objectives in Wind Turbines
Challenges of multiple objectives
  Designing individual controllers for each objective is getting more and more complex
  Conflicting with each other
  We need one controller that can balance all the objectives together
Notes: To reduce the overall cost, we have several…first we need the speed control to keep the rotor at the rated value when wind speed is very high. If the rotor is over-speed, it will cause the over-heat of the generator and make the turbine on fire as shown in the first figure.
Also we want the power control, to make sure we capture the maximum power from wind when wind speed is not that high.
In addition, we can see there are a lot of components failure, the tower may fall and blade may crack. We need to reduce the loads.
Also, the life of actuators has its limit, changing them too often will increase more costs. So that we need to prolong the actuator life.
However,…..it is quite challenging when we realize multiple objectives
In this research, we choose MPC to achieve the optimization….

## Slide 40
Control Architecture
Torque control: Standard torque control
Pitch control: Model predictive control
Yaw control: Not involved
-
Notes: The yaw control is not involved, similar to other studies.

## Slide 41
Model Predictive Controller (MPC)
: current time
: prediction horizon
: control horizon
Model predictive control (MPC): regulatory controls that use an explicit dynamic model of the response of process variables to changes in manipulated variables to calculate control “moves”
Control moves are intended to force the process variables to follow a pre-specified trajectory
Notes: This is an overview of model predictive controller, when we talk about MPC ,we are talking about using..
We have our manipulated variables , the planned control input
and we also have our process, the measured output and the past control input. We want to drive the predicted output close to the reference trajectory
What we are going to do is based on the information at time k to calculate the control input in the next step

## Slide 42
Predicted outputs
Model Predictive Controller (MPC)
Cost function
Notes: In order to predict the outputs, we need a prediction model. The model can be linear , nonlinear.. First principle model and hybrid models.. Here we use linear model from FAST.
The predicted outputs are a function of current state, past control input, future control input and unmeaured disturbances. The disturbance can be estimated by the Kalman filter.
What are we going to do next is using a cost function which can penalize the tracking error and control effort.

## Slide 43
Find
to minimize
subject to
Optimal solution
At time k:
Acquire new data
Estimate the current state x though Kalman filter
Solve the QP problem
and let be the solution
Apply only and discard the remaining inputs
Repeat optimization at time k+1, and so on…
Optimization steps:
Model Predictive Controller (MPC)
Notes: So the problem is to find an …..that is the control sequences of next m steps based on the information at time k
Upper and lower limits
Take the first move out of calculated control sequences to implemete. At next time step, everything shifts over by one, and recalculate moves based on the measurements at th samp
Since it is on-line optimization, the controller can reject the Unmeasured disturbances , and the influence the process model errors can be taken care of

## Slide 44
Switching Region Performance
Results:
Power: Nearly same
Speed : better
Tower fore-aft loads: reduced
Tower side-side loads: mixed
Blade edgewise loads: nearly same
Blade flapwise loads: reduced
Pitch actuator: reduced
Wind fields:
11 m/s, 12 m/s, 13 m/s

## Slide 45
Adaptive Controller
Challenges for wind turbine systems:
Complex dynamics
Uncertain environments
Difficulties in designing controller:
System parameters not completely known
Source: Liebherr
inherent model nonlinearities
unmodeled modes
manufacturing and assemblage tolerances
external operating uncertainties
Objective:
Generator speed at rated value and reduce oscillation
Mitigate loads
Near-term performance(constant speed)
Long-term reliability (less failure)
Adaptive Controller
Notes: Here comes our proposed adaptive controller, challenges…. Complx…and uncertain….
The large flexible structure operate in uncertain enviroments may have a lot unexpected failure
So the objective….
But there are diffculties to design such a contro….
We can not com….know sytem…due to..

## Slide 46
Method:
Model reference adaptive control (MRAC) with a disturbance accommodation controller (DAC): Two-layer structure
Control layer 1: DAC layer (closed-loop DAC: reference model)
disturbance accommodation
optimal trade-off between power capture and load mitigation
Control layer 2: Adaptive control layer
adapt to internal and external uncertainties
Adaptive Controller
Layer 2
Layer 1
Notes: This is our new attempt to tackle the problem…We adopt model…This is a two-layer..
The ..layer 1 is a …..We choose …as…The function of DAC is to achieve…
The disadvantage is that control performance can not be guaranteed when the turbine is not working near selected operating point.
So We will control layer 2 …to…
Next we will go through the details in layer 1 and layer 2

## Slide 47
Control Layer 2: Adaptive Approach
Adaptive control law
Theoretical assumption:
Actual wind turbine: linear, time-invariant, finite dimensional plant
Limitations of DAC
Not designed to be robust
May sensitive to errors in the turbine model
Adaptive control
Consider uncertainties: varying wind speed, unmodeled dynamics, and nonlinear aerodynamic loads
Layer 2
Notes:     Next we will introduce the layer 2, the adaptive approach. The reason we add this layer at the top of DAC is the limitationd of DAC under internal and external uncertaines. . Robust to the time-varying wind speed. It also may..
    The adaptive control can perfectly deal with these uncertainties. We use the closed-loop output of DAC as our reference signal and The nonlinear tuebine output as our plant output. The error between them is fed into the adaptive updating scheme. It consists of the error, state variable, control input and distruabnce. The on-line updating of gains can help deal with the uncertaities.

## Slide 48
The flapwise moment of GSPI from 360 s to 480 s is much higher compared to DAC and adaptive control
Flapwise moment: 9% reduce
Max flap moment: 11% reduce
Case Study: Results
Case 1: Mean wind speed 15 m/s
Notes: The mean wind speed of turbu field is 15

## Slide 49
Results
Flap DEL (damage equivalent load) :
12 m/s 21%-23% reduce
15 m/s 20%-28% reduce
17 m/s 21%-31% reduce
Generator speed RMS error:
Adaptive control is better than DAC, worse than GSPI
Discussion:
Larger load reduction: GSPI, no consideration of model uncertainties
Speed regulation: GSPI only for speed regulation, no efforts on others
Adaptive: speed regulation & load mitigation
Performance under Structural Uncertainties
Notes: Here are the results under sturactual uncertainties.
No consida…
The reason that load reduction is more than healthy condition is that
So the load reduction here is better than the health situation
So overall,adaptive control can have a gppd trade off

## Slide 50
Questions?
The End
Notes: Thank you

## Slide 51
Gain Scheduling PID
: rated power
: power

## Slide 52
Persistent wind disturbance input:
step disturbance
DOB backup1
Wind disturbance: Variance between nominal wind speed and the operating wind speed
unknown amplitude, known waveform
Notes: We assume in this reseach, dot
Take z transform of step. And from the loop shaping of previuos control sheckem,
So under the step disturbance, we can derive the expression of d

## Slide 53
DOB backup2
Step disturbance goes through disturbance model
Disturbance rejection is achieved if
0
: FIR filter, ensure causality of Q filter
: tune the local loop shaping based on the damped pole – zero pair principle
Notes: The FIR filter K is added to ensure the causality of Q
We also introduce an extra item in the denominator, where the design of belta is used to tune the local loop shaping. based on the damped pole –zero pair pinciple.
The effect of the choice of belta will be explained in details later.
When there is no belta, the shape of Q is certain ,we can not tune it. Belta can change the shape of Q, then we can tune it. Look at the figure.

## Slide 54
Stability and Robustness
No mismatch
between actual model and nominal model
bounded perturbed model uncertainty:
Mismatch
Stability Robustness [5]
[5] Doyle et al., Feedback Control Theory, 1990.
Notes: Previously we mentioned that the new controller is an augmented controller, will it still be stable and have perfect tracking of the reference signal?
This figure is an equivalent structure of the original controller.
The uncertainty can be bounded as
Based on the robust control theory, we can derive the condition for stability roubustness
This criteria can guide us designing the Q filter

## Slide 55
Nonlinear plant model