## Slide 1: Disturbance Observer Based Control Design for Wind Turbine Speed Regulation
Yuan Yuan, Xu Chen, and Jiong Tang
Oct 12, 2016
ASME Dynamic Systems and Control Conference 2016
Department of Mechanical Engineering
University of Connecticut
Storrs, CT, USA
Structure and System Dynamic Research Laboratory
Notes: Good afternoon everyone; my name is Yuan Yuan, I’m a Ph.D. student at University of Connecticut. The title of my presentation is … this paper is co-authored by myself, Prof. Xu Chen and my advisor prof Jiong tang
1

## Slide 2
Research Objective
Outline
Background
Case Analysis
Concluding Remarks
Approach
Notes: This is an outline of my presentation, first, background

## Slide 3
Wind turbine control loops
  Generator torque control
  Blade pitch control
  Nacelle yaw control
Background: Wind Turbine and Control
Wind Energy
Fastest growing energy source in the world: The worldwide wind capacity reached over 400,000 MW by the end of 2015
Low cost & Renewable
http://www.wavege.com/wind-turbine-diagram.html
Notes: It is well known that wind energy is the fastest ….
It is also low cost and renewable.
One important aspect of wind turbine is its control system. Let’s take a look at the control mechanism of a typical wind turbine.
This… this….Wind produce aerodynamic force and moments to the blade. It will drive rotor to rotate. the low speed shaft connects with rotor, the speed is going through the gearbox, and here is high speed shaft. The generator produces electricity.
There are 3 separate loops here. The first one is ….
In this research I focus on … which are most commonly studied in high wind speeds
//generator change the frequncey

## Slide 4
Increasing turbine size
  More frequent maintenance
Time-varying wind speed
  The plant dynamics are varying
      Control Goals
  Decrease the fluctuations of the generator speed and output power in time-varying wind speed
  Mitigate the structural fatigue to decrease the maintenance cost
Challenges of wind turbine
Source: DOE
Notes: There are some major challenges of wind turbine
One is the increasing turbine size: wind turbines have gotten progressively larger over the past 30 years. It can increase generation capacity and drive down costs. However, the larger size leads to more frequent maintenance.
The second is ……. We should design control laws to increase power capture at varying wind field.

## Slide 5
Research Objective
Outline
Background
Case Analysis
Concluding Remarks
Approach

## Slide 6
Research Objective
  Obtain the rated generator speed
  Control laws
    Baseline PID control [1]
    Disturbance accommodating control [2]
    Feedforward control [3]
    Adaptive control [4]
    Disturbance observer based control
Overall objective: Decrease generator speed fluctuation and output power fluctuation in Region 3
[1] Jonkman et al., National Renewable Energy Laboratory Technical Report, 2009.
[2] Wright, National Renewable Energy Laboratory Technical Report, 2004.
[3] Wang et al., IEEE Transactions on Control Systems Technology, 2012.
[4] Frost et al., International Journal of Robust and Nonlinear Control, 2009.
Notes:     Wind operating conditions are traditionally divided into 3 regions
    This figure shows the operating regions…
    In Region 1, the wind speed is very low, turbine did not start, there is no power.
    In Region 2, Blade pitch angle is held optimal constant.
    In Region 3 we want the generator power is held at a constant value.
    Specifically, what we want to achieve is ….in region 3…. In this research, we propose the disturbance observer based controller to achieve this goal. And compare it with the
DAC cancel out the disturabnce by eliminating the coeffciate of disturbance state
Feedfprward control employs a wind speed sensor , LIDAR to neasure wind speed can cancel out it in feedfowrad loop.
Ada.. Can force the nominal output to track the ref. output without knowing the accurate model

## Slide 7
Approach
Outline
Background
Research Objective
Case Analysis
Concluding Remarks

## Slide 8
AeroDyn
An aero-elastic simulation code (by NREL) to predict the aerodynamics
Input: steady or turbulent wind file
Output: force and moment on the turbine components
Nonlinear Aerodynamics
: mass matrix
: force
: control input
: wind input
: DOF displacements
: DOF velocities
: DOF accelerations
: time
Nonlinear aero-elastic equations of motion of wind turbine system
Notes: In order to get a proper model to design the controller,
we use the AeroDyn code to….. The input are wind file, turbine geometry, airfoil files and so on.
The output is force ……
The nonlinear …..is in this from. q .. F.. U.. Ud..
M is mass matrix, it is related to q, u, t that is because of different coordinates we use.
//which is independent, wind speed, pitch angle
which is not: rotor speed

## Slide 9
    linearization
FAST (Fatigue, Aerodynamics, Structures, Turbulence)
    FAST code (by NREL) used for simulating the coupled dynamic responses of wind turbines
Model Linearization
    State space representation
    Numerically linearize the equation by perturbing (∆) each variable about their respective operating points (op):
Notes: Then we can link it to FAST code to do linearization
FAST numerically …and substituting it to the previous nonlinear equation of motion
after Taylor series expansion. We could get the standard linearized form
And this is the state space form, delta ud is disturbance from the wind speed at operating point
So we have got the linearized model
(DspCis the displacement output matrix VelCis the velocity output matrix)

## Slide 10
Baseline Gain Scheduling Proportional Integral Derivative pitch controller [1]
Baseline Pitch Control
: small perturbation of blade pitch angle about the operating point
: error between measured generator speed and rated set point value
Gain scheduling factor to accommodate time-varying operating wind condition
: blade pitch angle at which the pitch sensitivity is doubled from its value at the rated operating point.
Gain scheduling: , are changed
[1] Jonkman et al., National Renewable Energy Laboratory Technical Report, 2009.
.
Notes: Now let’s move to the baseline pitch control
Different from the classical PID control, we add a gain scheduled factor to …. part which is a function of pitch angle.
That is the gs part, we can change the PID gains when wind speed is varying. Because PID gains are tuned at Op, which can not gurantee the perfect performance at time-varying wind field.
After the PID gains, we also add the mechanical limits of pitch actuator in the block..
(Pitch actuator: 30HZ)

## Slide 11
Disturbance observer based controller
Why this controller?
PID controller: gains are tuned in rated wind, but time-varying wind speed
Gain-scheduling PID: perfect gain correction is not strictly guaranteed
Augmented controller: inner-loop can further reject low frequency disturbance based on the disturbance suppression of the outer-loop.
:
wind disturbance
:
disturbance model
:
plant model
:
model inversion
:
filter
:
PID controller
directly cancels out
filter Q
0
den
num
Notes: Now let’s move to the disturbance obersver….
It is an inverse-based disturbance cancelation scheme. We want to use d hat to directly cancel out d
The inner loop is the disturbance observer structure, the outter loop is the gain-scheduled PID controller. Both of them will contribute to disturbance rejection.
The P inverse should be stable
For any signal d it will satisfy this eq. where Bd is numerator of atransofrm of d. Ad is the corsponding den.

## Slide 12
Persistent wind disturbance input:
step disturbance
Disturbance Observer based controller
Wind disturbance: Variance between nominal wind speed and the operating wind speed
unknown amplitude, known waveform
Notes: We assume in this reseach, dot
Take z transform of step. And from the loop shaping of previuos control sheckem,
So under the step disturbance, we can derive the expression of d

## Slide 13
Disturbance Observer based controller
Step disturbance goes through disturbance model
Disturbance rejection is achieved if
0
: FIR filter, ensure causality of Q filter
: tune the local loop shaping based on the damped pole – zero pair principle
Notes: The FIR filter K is added to ensure the causality of Q
We also introduce an extra item in the denominator, where the design of belta is used to tune the local loop shaping. based on the damped pole –zero pair pinciple.
The effect of the choice of belta will be explained in details later.
When there is no belta, the shape of Q is certain ,we can not tune it. Belta can change the shape of Q, then we can tune it. Look at the figure.

## Slide 14
Stability and Robustness
No mismatch
between actual model and nominal model
bounded perturbed model uncertainty:
Mismatch
Stability Robustness [5]
[5] Doyle et al., Feedback Control Theory, 1990.
Notes: Previously we mentioned that the new controller is an augmented controller, will it still be stable and have perfect tracking of the reference signal?
This figure is an equivalent structure of the original controller.
The uncertainty can be bounded as
Based on the robust control theory, we can derive the condition for stability roubustness
This criteria can guide us designing the Q filter

## Slide 15
Approach
Outline
Background
Research Objective
Case Analysis
Concluding Remarks
Notes: Next we will present the case study results

## Slide 16
5-DOF linearized model
5 DOF: Generator DOF, drivetrain torsional flexiblity DOF, and first flapwise blade mode DOF (three blades)
Notes: To obtain the preliminary result of the DOB controller, we first apply the controller into the 5-DOF linearized model
These are the
The result seems to be promising, so how is it with the nonlinear plant

## Slide 17
Test wind turbine
  NREL offshore 5-MW baseline
  wind turbine
Degree of freedom (DOF)
  16 DOFs*
Turbulent wind field
Simulation time
  Run time: 0 to 600 s
  Integration step size: 0.0125 s
Blade pitch limit and pitch rate limit [1]
  Minimum/maximum blade pitch: 0 degree / 90 degree
  Maximum absolute blade pitch rate: 8 degree/s
Case Study: Nonlinear plant
Case study:
[1] Jonkman et al., 2009, National Renewable Energy Laboratory, Golden, CO.
*First flapwise blade mode (3 blades), second flapwise blade mode (3 blades), first edgewise blade mode (3 blades), drivetrain rotational-flexibility, generator, yaw, first fore-aft tower bending-mode, second fore-aft tower bending-mode, first side-to-side tower bending-mode, second side-to-side tower bending-mode.
Source:https://www.youtube.com/watch?v=h4KidjcDDis
Notes: The wind speed on each segment of blade is going to change with time.

## Slide 18
Nonlinear plant model

## Slide 19
under different
Trade-off in selection of Q filter
Trade-off between disturbance rejection region and disturbance amplification region:
Sensitivity function:
Disturbance amplification:
Instability of the nonlinear plant (model mismatch exists)[5]
[5] Doyle et al., Feedback Control Theory, 1990.
Notes: Here we will talk about how to make a trade off in selection of Q filter. Specifically it is the trade-off between ……
In practice, when DOB controller is applied to nonlinear controller, the disturbance amplification at high freuqencies will lead to the insatiability of …..
Actually the value of belta is related to sensitivity function. This equation in the red box is an indicator of sensitivity function. We check the fre response of it under differernt belta.
From the figure we can see the samller belta will lead to wider disturbance rejection region, but at the same time the larger disturbance amplification. Which will influence the stability of system.
Finally we choose belta =.997.

## Slide 20
Performance comparison
Results:
3.59% - 9.56% decrease in 6 wind fields
2.38% - 8.01% increase in 3 wind fields
Limited performance due to trade-off with respect to the stability issue
Notes: This slide shows the results based on the selected Q filter
The first figure is wind speed
The second figure is the …response under 18
We can see
To test robustness of the DOB controller, we applied it to wide wind speed region from 14 to 22.
We can find there is …..
So what more we can do?

## Slide 21
Add-on compensator
Sensitivity function
Smaller disturbance amplification at certain high frequencies in Q*
Better disturbance rejection in low freq.
Faster roll-off at high frequencies
Low pass filter
Q filter (DOB)
Q* filter (DOB*)
Notes: Next we will introduce how to improve the tracking perfromance. We propose to use an add-on compes

## Slide 22
Performance comparison
FFT

## Slide 23
Performance comparison
Normalized generator speed RMS error: -28.13% to -39.14%
Normalized power RMS error: -31.43% to -40.93%
Conclusion:
Enhanced generator speed and power regulation with DOB* in Region 3
Notes: We can obtain an obvious decrease

## Slide 24
Concluding Remarks
  A general disturbance observer (DOB) based controller tailored for wind turbine is developed;
  The FIR filter and a tuning factor are introduced to facilitate better design of Q filter;
  Generator speed and power regulation performance is enhanced in DOB* controller for the actual nonlinear wind turbine under turbulent wind filed;
  DOB controller shows stability robustness under the entire Region 3.
This research is supported by NSF under grant CMMI – 1300236
Notes: simulation software

## Slide 25
Questions?
The End
Notes: Thank you

## Slide 26
References
[1] Jonkman et al., Definition of a 5-MW reference wind turbine for offshore system development. 2009: National Renewable Energy Laboratory Golden, CO.
[2] Wright, Modern control design for flexible wind turbines. 2004: National Renewable Energy Laboratory Golden, CO, USA.
[3] Wang, Johnson and Wright. (2012). FX-RLS-based feedforward control for LIDAR-enabled wind turbine load mitigation. Control Systems Technology, IEEE Transactions on, 20(5), 1212-1222.
[4] Frost, Balas, and Wright. Adaptive Control of a Utility-Scale Wind Turbine Operating in Region 3. Proceedings of the 28th AIAA Aerospace Sciences Meeting and Exhibit Wind Energy Symposium. 2009.
[5] Chen and Tomizuka. An enhanced repetitive control algorithm using the structure of disturbance observer. Advanced Intelligent Mechatronics (AIM), 2012 IEEE/ASME International Conference on. IEEE, 2012.

## Slide 27
Gain Scheduling PID
: rated power
: power

## Slide 28
Region 2 Torque Control

## Slide 29
: GSPI, : DOB*.
Other results
RMS pitch rate
Average power
Loads on drive-train, blades and tower

## Slide 30
: aerodynamic torque
: power efficiency
: tip speed ratio
: air intensity
: wind speed
: rotor speed
:generator speed
low speed shaft torque
high speed shaft torque
generator electromagnetic torque
: rotor inertia
: generator inertia
: turbine total inertia
: rotor external damping
: generator external damping
: turbine total external damping
Simple Model
Aerodynamic torque
Rotor Dynamics and
generator dynamics
Gearbox ratio
Notes: In most of the literature, a simple model is adopted to design control method in order to get better speed regulation.
The aerodynamics… is a function of power efficiency, wind speed and rotor speed, it is highly nonlinear.
Assume the low speed shaft is rigid, the rotor dynamics and generator dynamics can be expressed as…
As the low speed shaft torque and HSS torque satisfy gearbox ratio relationship, finally we could get a simple equation of motion.
We can control the electromagnetic torque to track the generator speed. But it is hard to use this model to adjust blade pitch angle to achieve load reduction. Because here the pitch angle is contained in the nonlinear term Cp.

## Slide 31
Region 2 Standard Torque Control
Region 2 standard torque control
Generator Speed (rpm)
Generator Torque (N*m)
670
1161
1173
    No power
    Optimal constant blade pitch angle
    Rated generator speed
    Linear transition
Region 3
Region 2 1/2
Region 2
Region 1
TSR:
Notes: In Region 2, the control objective is to maximize the power capture. We use torque control to achieve it. Let us look at the Cp surface. We can see the maximum value is in pitch angle 0 tip speed ratio 7.5.
That is make the tip speed ratio be the optimal value, at the optimal pitch angle.
Then we should let the rotor speed track the wind speed. Here the pitch control is disabled, then we control torque to change rotor speed.
power Per second

## Slide 32
, =7.5
The curve (dotted line)
The solid line
, , , it will accelerate to
, rotor speed will slow to zero
How does it drive Region 2 to obtain maximum (Assume uniform constant wind)
, , rotor will decelerate towards
Region 2 standard torque control

## Slide 33
Generator torque controller
Torque Control
: generator speed
: optimal constant of proportionality (0.0255764)
: 1,161.963
: 1173.7
: 43,093.55
: 34532.18
Notes: That is the overall torque control in 3 regions…..
Actually the torque controller can be designed with adaptive control or sliding mode control to achieve better performance in the literature.
Here for this baseline controller,
In Region 1, torque is 0.
In region 2 ,torque is a function of generator speed. To maintain a constant optimal tip speed ratio
In region 2 and a half, it is a ……
In region 3 ,the torque is held at rated value

## Slide 35
Basic Concepts
For disturbance satisfying
(asymptotically)
Disturbance can be represented by z transform
0
Notes: Dk is the impulse response of this transfer function

## Slide 36
Unstable inversed model
Plant P may have nonminimum zeros. P inverse is not stable
Zero Phase Error Tracking (ZPET) method
  includes zeros of stable part, includes zeros of unstable part
Stable model inversion
Zero Phase Error Tracking method
Notes: Usually in the modern commercial wind turbine,

## Slide 37
Bode of PID
Notes: What Q cut-off freq. means? Reject the disturbance smaller than this?
0.9952 . Smaller than this, it diverge

## Slide 38
Pitch angle
Wind turbine starts()
Wind turbine stops(90)
rotor plane
Low speed shaft horizontal axis
Notes: Pitch angle is the angle between chord line and rotor plane

## Slide 39
Turbulent wind field

## Slide 41
Flapwise shear force and moment
Wind
Flapwise shear force at the blade root:
Directed along the axis (kN)
Flapwise moment at the blade root :
About the axis (kN*m)
Notes: Perpendicular
parallel

## Slide 42
Blade-pitch sensitivity
  aerodynamic property of the rotor that depends on the wind speed, rotor speed, and blade-pitch angle
  perturb the rotor collective blade pitch angle at each operating point and measure the resulting variation in aerodynamic power
Table Sensitivity of Aerodynamic Power to Blade Pitch in Region 3
Wind speed (m/s) | Rotor Speed (rpm) | Pitch Angle (deg) | (watt/rad)
11.4-Rated | 12.1 | 0.00 | -28.24E+6
12.0 | 12.1 | 3.83 | -43.73E+6
13.0 | 12.1 | 6.60 | -51.66E+6
14.0 | 12.1 | 8.70 | -58.44E+6
15.0 | 12.1 | 10.45 | -64.44E+6
16.0 | 12.1 | 12.06 | -70.46E+6
17.0 | 12.1 | 13.54 | -76.53E+6
18.0 | 12.1 | 14.92 | -83.94E+6
19.0 | 12.1 | 16.23 | -90.71E+6
20.0 | 12.1 | 17.47 | -94.71E+6
21.0 | 12.1 | 18.70 | -99.04E+6
22.0 | 12.1 | 19.94 | -105.90E+6
23.0 | 12.1 | 21.18 | -114.30E+6
24.0 | 12.1 | 22.35 | -120.20E+6
25.0 | 12.1 | 23.47 | -125.30E+6
Wind speed (m/s) | Rotor Speed (rpm) | Pitch Angle (deg) | 
11.4-Rated | 12.1 | 0.00 | -28.24E+6
12.0 | 12.1 | 3.83 | -43.73E+6
13.0 | 12.1 | 6.60 | -51.66E+6
14.0 | 12.1 | 8.70 | -58.44E+6
15.0 | 12.1 | 10.45 | -64.44E+6
16.0 | 12.1 | 12.06 | -70.46E+6
17.0 | 12.1 | 13.54 | -76.53E+6
18.0 | 12.1 | 14.92 | -83.94E+6
19.0 | 12.1 | 16.23 | -90.71E+6
20.0 | 12.1 | 17.47 | -94.71E+6
21.0 | 12.1 | 18.70 | -99.04E+6
22.0 | 12.1 | 19.94 | -105.90E+6
23.0 | 12.1 | 21.18 | -114.30E+6
24.0 | 12.1 | 22.35 | -120.20E+6
25.0 | 12.1 | 23.47 | -125.30E+6
Pitch Sensitivity

## Slide 43
Torque control: Choose the appropriate stator current according to the difference of reference torque and actual torque
Control structure of a permanent magnet synchronous generator system for use in wind turbines
Notes: Stator coils
Rotor magnet

## Slide 45
Step wind from 17 m/s to 21 m/s Turbulent 18 m/s wind field