## Slide 1: Application of Model Predictive Control for Optimal Operation of Wind Turbines
Yuan Yuan, Pei Cao, and Jiong Tang
Mar 27, 2017
SPIE Smart Structures NDE Conference 2017
Department of Mechanical Engineering
University of Connecticut
Storrs, CT, USA
Dynamics, Sensing, and Controls Laboratory
Notes: Good afternoon everyone; my name is Yuan Yuan, I’m a Ph.D. student at University of Connecticut. The title of my presentation is … this paper is co-authored by myself, pei cao and my advisor prof Jiong tang
1

## Slide 2
Research Objective
Outline
Background
Case Analysis
Concluding Remarks
Approach
Notes: This is an outline of my presentation, first, background, and then research objective,…….

## Slide 3
Wind turbine control loops
  Generator torque control
  Blade pitch control
  Nacelle yaw control
Background: Wind Turbine and Control
Wind Energy
Fastest growing energy source in the world: The worldwide wind capacity reached over 400,000 MW by the end of 2015
Low cost & Renewable
http://www.wavege.com/wind-turbine-diagram.html
Notes: It is well known that wind energy is the fastest ….
It is also low cost and renewable.
One important aspect of wind turbine is the control system. Let’s take a look at the control mechanism of a typical wind turbine.
Wind will produce aerodynamic force and moments to the blade. It will drive rotor to rotate. The generator produces electricity.
There are 3 separate loops here. The first one is ….
In this research I focus on … which are most commonly studied in high wind speeds
//generator change the frequncey

## Slide 4
Increased turbine size
  More frequent maintenance
Time-varying wind speed
  The plant dynamics are varying
      Reduce overall costs
  More power capture
  Lower maintenance cost
Challenges of Wind Turbine
Source: DOE
Notes: There are some major challenges of wind turbine
One is the increasing turbine size: wind turbines have gotten progressively larger over the past 30 years. It can increase generation capacity and drive down costs. However, the larger size leads to more frequent maintenance.
The second is …….
An important problem in application is that how to reduce overall cost. That is

## Slide 5
Different control goals
Speed control
Power control
Load reduction on blades, tower and drive-train
Prolong actuator life
      Model predictive control:
      Online optimization of multiple control objectives
Multiple Objectives in Wind Turbines
Challenges of multiple objectives
  Designing individual controllers for each objective is getting more and more complex
  Conflicting with each other
  We need one controller that can balance all the objectives together
Notes: To reduce the overall cost, we have several…first we need the speed control to keep the rotor at the rated value when wind speed is very high. If the rotor is over-speed, it will cause the over-heat of the generator and make the turbine on fire as shown in the first figure.
Also we want the power control, to make sure we capture the maximum power from wind when wind speed is not that high.
In addition, we can see there are a lot of components failure, the tower may fall and blade may crack. We need to reduce the loads.
Also, the life of actuators has its limit, changing them too often will increase more costs. So that we need to prolong the actuator life.
However,…..it is quite challenging when we realize multiple objectives
In this research, we choose MPC to achieve the optimization….

## Slide 6
Research Objective
Outline
Background
Case Analysis
Concluding Remarks
Approach

## Slide 7
Research Objective
  Maintain the rated generator speed
  Follow the actuator constraints
  Maximize power capture
  Mitigate blade and tower loads
Optimization of multiple objectives in the switching region and Region 3
[1] Jonkman et al., National Renewable Energy Laboratory Technical Report, 2009.
  Multiple objectives
  Control laws
    Baseline PID control [1]
    Model predictive control
Notes:     Wind operating conditions are traditionally divided into 3 regions
    This figure shows the operating regions…
    In Region 1, the wind speed is very low, turbine did not start, there is no power.
    In Region 2, Blade pitch angle is held optimal constant.
    In Region 3 we want the generator power is held at a constant value.
    The switching region is between Region 2 and 3.
    We have multiple objectives…
    So the research objective is to achieve ………

## Slide 8
Approach
Outline
Background
Research Objective
Case Analysis
Concluding Remarks

## Slide 9
AeroDyn
An aero-elastic simulation code (by NREL) to predict the aerodynamics
Input: steady or turbulent wind file
Output: force and moment on the turbine components
Nonlinear Aerodynamics
: mass matrix
: force
: control input
: wind input
: DOF displacements
: DOF velocities
: DOF accelerations
: time
Nonlinear aero-elastic equations of motion of wind turbine system
Notes: In order to get a proper model to design the controller,
we use the AeroDyn code to….. The input are wind file, turbine geometry, airfoil files and so on.
The output is force ……
The nonlinear …..is in this from. q .. F.. U.. Ud..
M is mass matrix, it is related to q, u, t that is because of different coordinates we use.
//which is independent, wind speed, pitch angle
which is not: rotor speed

## Slide 10
    linearization
FAST (Fatigue, Aerodynamics, Structures, Turbulence)
    FAST code (by NREL) used for simulating the coupled dynamic responses of wind turbines
Model Linearization
    State space representation
    Numerically linearize the equation by perturbing (∆) each variable about their respective operating points (op):
Notes: Then we can link it to FAST code to do linearization
FAST numerically …and substituting it to the previous nonlinear equation of motion
after Taylor series expansion. We could get the standard linearized form
And this is the state space form, delta ud is disturbance from the wind speed at operating point
So we have got the linearized model
(DspCis the displacement output matrix VelCis the velocity output matrix)

## Slide 11
Control Architecture
Torque control: Standard torque control
Pitch control: Model predictive control
Yaw control: Not involved
-
Notes: The yaw control is not involved, similar to other studies.

## Slide 12
Generator torque controller
Standard Torque Control
: generator speed
: optimal constant of proportionality (0.0255764)
: 1,161.963
: 1173.7
: 43,093.55
: 34532.18
Notes: That is the overall torque control in 3 regions…..
Actually the torque controller can be designed with adaptive control or sliding mode control to achieve better performance in the literature.
Here for this baseline controller,
In Region 1, torque is 0.
In region 2 ,torque is a function of generator speed. To maintain a constant optimal tip speed ratio
In region 2 and a half, it is a ……
In region 3 ,the torque is held at rated value

## Slide 13
Model Predictive Controller (MPC)
: current time
: prediction horizon
: control horizon
Model predictive control (MPC): regulatory controls that use an explicit dynamic model of the response of process variables to changes in manipulated variables to calculate control “moves”
Control moves are intended to force the process variables to follow a pre-specified trajectory
Notes: This is an overview of model predictive controller, when we talk about MPC ,we are talking about using..
We have our manipulated variables , the planned control input
and we also have our process, the measured output and the past control input. We want to drive the predicted output close to the reference trajectory
What we are going to do is based on the information at time k to calculate the control input in the next step

## Slide 14
Predicted outputs
Model Predictive Controller (MPC)
Cost function
Notes: In order to predict the outputs, we need a prediction model. The model can be linear , nonlinear.. First principle model and hybrid models.. Here we use linear model from FAST.
The predicted outputs are a function of current state, past control input, future control input and unmeaured disturbances. The disturbance can be estimated by the Kalman filter.
What are we going to do next is using a cost function which can penalize the tracking error and control effort.

## Slide 15
Find
to minimize
subject to
Optimal solution
At time k:
Acquire new data
Estimate the current state x though Kalman filter
Solve the QP problem
and let be the solution
Apply only and discard the remaining inputs
Repeat optimization at time k+1, and so on…
Optimization steps:
Model Predictive Controller (MPC)
Notes: So the problem is to find an …..that is the control sequences of next m steps based on the information at time k
Upper and lower limits
Take the first move out of calculated control sequences to implemete. At next time step, everything shifts over by one, and recalculate moves based on the measurements at th samp
Since it is on-line optimization, the controller can reject the Unmeasured disturbances , and the influence the process model errors can be taken care of

## Slide 16
Selection of Design Parameters
Prediction horizon, p
Diagonal matrices with larger elements corresponding to most important variables
Control horizon m
Larger p results in less aggressive control action
Larger m makes the controller more aggressive and increase computational effort, typically
Weighting matrices Q and R

## Slide 17
Approach
Outline
Background
Research Objective
Case Analysis
Concluding Remarks
Notes: Next we will present the case study results

## Slide 18
Test wind turbine
  NREL offshore 5-MW baseline
  wind turbine
Degree of freedom (DOF)
  16 DOFs*
Turbulent wind field
Simulation time
  Run time: 0 to 600 s
  Integration step size: 0.0125 s
Blade pitch limit and pitch rate limit [1]
  Minimum/maximum blade pitch: 0 degree / 90 degree
  Maximum absolute blade pitch rate: 8 degree/s
Case Study: Nonlinear plant
Case study:
[1] Jonkman et al., 2009, National Renewable Energy Laboratory, Golden, CO.
*First flapwise blade mode (3 blades), second flapwise blade mode (3 blades), first edgewise blade mode (3 blades), drivetrain rotational-flexibility, generator, yaw, first fore-aft tower bending-mode, second fore-aft tower bending-mode, first side-to-side tower bending-mode, second side-to-side tower bending-mode.
Source:https://www.youtube.com/watch?v=h4KidjcDDis
Notes: The wind speed on each segment of blade is going to change with time.

## Slide 19
Nonlinear plant model

## Slide 20
Switching Region Performance
Results:
Power: Nearly same
Speed : better
Tower fore-aft loads: reduced
Tower side-side loads: mixed
Blade edgewise loads: nearly same
Blade flapwise loads: reduced
Pitch actuator: reduced
Wind fields:
11 m/s, 12 m/s, 13 m/s

## Slide 21
Region 3 Performance
Results:
Power: Nearly same
Speed : better
Tower fore-aft loads: increased
Tower side-side loads: increased
Blade edgewise loads: nearly same
Blade flapwise loads: increased
Pitch actuator: increased
Wind fields:
16 m/s, 18 m/s, 20 m/s

## Slide 22
Concluding Remarks
  A general model predictive controller tailored for wind turbine is developed;
  Optimization of multiple objectives in the switching region and Region 3;
  Switching region: loads on blades and tower can be reduced, actuator usage is reduced and power is nearly same;
  Region 3: loads and actuator usage are deteriorated.
This research is supported by NSF under grant CMMI – 1300236

## Slide 23
Questions?
The End
Notes: Thank you

## Slide 24
Gain Scheduling PID
: rated power
: power

## Slide 25
Standard Torque Control
Region 2 standard torque control
Generator Speed (rpm)
Generator Torque (N*m)
670
1161
1173
    No power
    Optimal constant blade pitch angle
    Rated generator speed
    Linear transition
Region 3
Region 2 1/2
Region 2
Region 1
TSR:
Notes: In Region 2, the control objective is to maximize the power capture. We use torque control to achieve it. Let us look at the Cp surface. We can see the maximum value is in pitch angle 0 tip speed ratio 7.5.
That is make the tip speed ratio be the optimal value, at the optimal pitch angle.
Then we should let the rotor speed track the wind speed. Here the pitch control is disabled, then we control torque to change rotor speed.
power Per second

## Slide 26
Region 2 Torque Control

## Slide 27
: aerodynamic torque
: power efficiency
: tip speed ratio
: air intensity
: wind speed
: rotor speed
:generator speed
low speed shaft torque
high speed shaft torque
generator electromagnetic torque
: rotor inertia
: generator inertia
: turbine total inertia
: rotor external damping
: generator external damping
: turbine total external damping
Simple Model
Aerodynamic torque
Rotor Dynamics and
generator dynamics
Gearbox ratio
Notes: In most of the literature, a simple model is adopted to design control method in order to get better speed regulation.
The aerodynamics… is a function of power efficiency, wind speed and rotor speed, it is highly nonlinear.
Assume the low speed shaft is rigid, the rotor dynamics and generator dynamics can be expressed as…
As the low speed shaft torque and HSS torque satisfy gearbox ratio relationship, finally we could get a simple equation of motion.
We can control the electromagnetic torque to track the generator speed. But it is hard to use this model to adjust blade pitch angle to achieve load reduction. Because here the pitch angle is contained in the nonlinear term Cp.

## Slide 28
, =7.5
The curve (dotted line)
The solid line
, , , it will accelerate to
, rotor speed will slow to zero
How does it drive Region 2 to obtain maximum (Assume uniform constant wind)
, , rotor will decelerate towards
Region 2 standard torque control

## Slide 29
Generator torque controller
Torque Control
: generator speed
: optimal constant of proportionality (0.0255764)
: 1,161.963
: 1173.7
: 43,093.55
: 34532.18
Notes: That is the overall torque control in 3 regions…..
Actually the torque controller can be designed with adaptive control or sliding mode control to achieve better performance in the literature.
Here for this baseline controller,
In Region 1, torque is 0.
In region 2 ,torque is a function of generator speed. To maintain a constant optimal tip speed ratio
In region 2 and a half, it is a ……
In region 3 ,the torque is held at rated value

## Slide 30
Bode of PID
Notes: What Q cut-off freq. means? Reject the disturbance smaller than this?
0.9952 . Smaller than this, it diverge

## Slide 31
Pitch angle
Wind turbine starts()
Wind turbine stops(90)
rotor plane
Low speed shaft horizontal axis
Notes: Pitch angle is the angle between chord line and rotor plane

## Slide 32
Turbulent wind field

## Slide 33
Flapwise shear force and moment
Wind
Flapwise shear force at the blade root:
Directed along the axis (kN)
Flapwise moment at the blade root :
About the axis (kN*m)
Notes: Perpendicular
parallel

## Slide 34
Blade-pitch sensitivity
  aerodynamic property of the rotor that depends on the wind speed, rotor speed, and blade-pitch angle
  perturb the rotor collective blade pitch angle at each operating point and measure the resulting variation in aerodynamic power
Table Sensitivity of Aerodynamic Power to Blade Pitch in Region 3
Wind speed (m/s) | Rotor Speed (rpm) | Pitch Angle (deg) | (watt/rad)
11.4-Rated | 12.1 | 0.00 | -28.24E+6
12.0 | 12.1 | 3.83 | -43.73E+6
13.0 | 12.1 | 6.60 | -51.66E+6
14.0 | 12.1 | 8.70 | -58.44E+6
15.0 | 12.1 | 10.45 | -64.44E+6
16.0 | 12.1 | 12.06 | -70.46E+6
17.0 | 12.1 | 13.54 | -76.53E+6
18.0 | 12.1 | 14.92 | -83.94E+6
19.0 | 12.1 | 16.23 | -90.71E+6
20.0 | 12.1 | 17.47 | -94.71E+6
21.0 | 12.1 | 18.70 | -99.04E+6
22.0 | 12.1 | 19.94 | -105.90E+6
23.0 | 12.1 | 21.18 | -114.30E+6
24.0 | 12.1 | 22.35 | -120.20E+6
25.0 | 12.1 | 23.47 | -125.30E+6
Wind speed (m/s) | Rotor Speed (rpm) | Pitch Angle (deg) | 
11.4-Rated | 12.1 | 0.00 | -28.24E+6
12.0 | 12.1 | 3.83 | -43.73E+6
13.0 | 12.1 | 6.60 | -51.66E+6
14.0 | 12.1 | 8.70 | -58.44E+6
15.0 | 12.1 | 10.45 | -64.44E+6
16.0 | 12.1 | 12.06 | -70.46E+6
17.0 | 12.1 | 13.54 | -76.53E+6
18.0 | 12.1 | 14.92 | -83.94E+6
19.0 | 12.1 | 16.23 | -90.71E+6
20.0 | 12.1 | 17.47 | -94.71E+6
21.0 | 12.1 | 18.70 | -99.04E+6
22.0 | 12.1 | 19.94 | -105.90E+6
23.0 | 12.1 | 21.18 | -114.30E+6
24.0 | 12.1 | 22.35 | -120.20E+6
25.0 | 12.1 | 23.47 | -125.30E+6
Pitch Sensitivity

## Slide 35
Torque control: Choose the appropriate stator current according to the difference of reference torque and actual torque
Control structure of a permanent magnet synchronous generator system for use in wind turbines
Notes: Stator coils
Rotor magnet